## Slide 1: Data-Driven Quality Improvement in Beverage Manufacturing A Lean Six Sigma Approach Using Control Charts and Root Cause Analysis

## Slide 2
Introduction to the Process & Problem Context

## Slide 3
The production runs across two shifts daily (Morning and Evening), managed by a team of four trained operators using three different machines (PX1, PX2, PX3).
Each unit must meet a strict net weight specification of 500g ±5g, which ensures compliance with quality standards and customer expectations.
It produces three product lines Aloe Juice, Energy Drink, and Protein Shake using automated filling and packaging machines
The company operates in the fast-moving consumer goods (FMCG) sector, specifically in non-carbonated beverage production

## Slide 4
The production runs across two shifts daily (Morning and Evening), managed by a team of four trained operators using three different machines (PX1, PX2, PX3).
Each unit must meet a strict net weight specification of 500g ±5g, which ensures compliance with quality standards and customer expectations.
It produces three product lines Aloe Juice, Energy Drink, and Protein Shake using automated filling and packaging machines
The company operates in the fast-moving consumer goods (FMCG) sector, specifically in non-carbonated beverage production

## Slide 5
The production runs across two shifts daily (Morning and Evening), managed by a team of four trained operators using three different machines (PX1, PX2, PX3).
Each unit must meet a strict net weight specification of 500g ±5g, which ensures compliance with quality standards and customer expectations.
The company operates in the fast-moving consumer goods (FMCG) sector, specifically in non-carbonated beverage production
It produces three product lines Aloe Juice, Energy Drink, and Protein Shake using automated filling and packaging machines

## Slide 6
The production runs across two shifts daily (Morning and Evening), managed by a team of four trained operators using three different machines (PX1, PX2, PX3)
The company operates in the fast-moving consumer goods (FMCG) sector, specifically in non-carbonated beverage production
It produces three product lines Aloe Juice, Energy Drink, and Protein Shake using automated filling and packaging machines
Each unit must meet a strict net weight specification of 500g ±5g, which ensures compliance with quality standards and customer expectations.

## Slide 7
Problem Context
Recent data shows a significant increase in defects,
especially in the Energy Drink and Protein Shake lines.

## Slide 8
Problem Context
Recent data shows a significant increase in defects,
especially in the Energy Drink and Protein Shake lines.
Main defect types identified Underfilled bottles (less than 495g)

## Slide 9
Six Sigma & Lean Six Sigma
Approach

## Slide 10
What is Six Sigma?
A quality management method

## Slide 11
What is Six Sigma?
A quality management method
Focused on process improvement

## Slide 12
What is Six Sigma?
A quality management method
Focused on process improvement
Uses data and statistics to reduce errors

## Slide 13
What is Six Sigma?
A quality management method
Focused on process improvement
Uses data and statistics to reduce errors
Metrics :- DPMO, Sigma Level, Higher Sigma

## Slide 14
Objective of Six Sigma
Reduce defects in processes

## Slide 15
Objective of Six Sigma
Reduce defects in processes
Minimize variation

## Slide 16
Objective of Six Sigma
Reduce defects in processes
Minimize variation
Improve consistency and quality

## Slide 17
What is Lean Six Sigma?
Combines Lean (removing waste) + Six Sigma (controlling variation)

## Slide 18
What is Lean Six Sigma?
Combines Lean (removing waste) + Six Sigma (controlling variation)
Focuses on efficiency + quality

## Slide 19
Key Benefits of Lean Six Sigma
Faster processes with fewer delays

## Slide 20
Key Benefits of Lean Six Sigma
Faster processes with fewer delays
Higher product or service quality

## Slide 21
Key Benefits of Lean Six Sigma
Faster processes with fewer delays
Higher product or service quality
Better customer satisfaction

## Slide 22
Key Benefits of Lean Six Sigma
Faster processes with fewer delays
Higher product or service quality
Better customer satisfaction
Cost savings

## Slide 23
Six Sigma Problem-Solving Approach: DMAIC, DMADC

## Slide 24
CONTROL
IMPROVE
ANALYSE
MEASURE
DMAIC stands for Define, Measure, Analyze, Improve, Control. It is a structured problem-solving approach used in Six Sigma projects for continuous improvement
What is DMAIC

## Slide 25
D
I
A
M
C
Define
Clearly defines the problem and
sets project goals
Measure
Collects data to measure current performance
Analyze
Identifies root causes of the problem
Improve
Develops solutions to improve the process
Control
Ensures the improvements are sustained

## Slide 26
VERIFY
DESIGN
ANALYSE
MEASURE
DMADV stands for Define, Measure, Analyze, Design, Verify. It is a structured methodology used in Six Sigma for designing new processes or products.
What is DMAIC

## Slide 27
D
D
A
M
V
Define
Clearly define the problem and project goals
Measure
Collect data to understand the
current process
Analyze
Identify root causes and analyze potential solutions
Design
Design the new process or product to meet customer needs
Verify
Validate the new design by testing and ensuring it meets specifications

## Slide 28
Control Charts Overview

## Slide 29
When to Use the Basic Control Charts
Variable data
Attribute Data
X bar and R chart
X bar and S chart
Defects
Defectives
P chart
nP chart
U chart
C chart
What is a Control Chart?

## Slide 30
Control vs. Out of Control
In Control
When the process data points consistently fall within the control limits (UCL and LCL), the process is said to be "In Control”
Out of Control
When data points fall outside the control limits or exhibit non-random patterns, the process is "Out of Control"

## Slide 31
Fishborn Diagram Overview

## Slide 32
Fishbone Diagram
Problem
Material
Measurement
Machine
Method
Environment
Employee
Quality of Raw Materials
Contamination
Inaccurate Instruments
Human Error
Poor Maintenance
Machine Calibration
Process Complexity
Process Complexity
Temperature and Humidity
Air Quality
Lack of Training
Skill Level

## Slide 33
Sampling Technique Overview
Select the Sample

## Slide 34: Random Sampling
Commonly used in surveys, experiments and observational studies
Ensure unbiased representation
Helps collect reliable data

## Slide 35: Random Sampling
Allows for the generalisation of results to the larger population
Increases the validity of the findings
Straightforward to implement
Applications
Commonly used in surveys, experiments and
observational studies
Ensure unbiased representation
Helps collect reliable data

## Slide 36: Systematic Sampling
Ensures good population coverage
More convenient than random sampling

## Slide 37: Systematic Sampling
Ensures good population coverage
More convenient than random sampling
Applications
Commonly used in quality control processes
Often applied to ordered populations, such as
    Time series data
    Sequential production outputs

## Slide 38: Cluster Sampling
Cost-effective
Time-saving
Especially beneficial for large populations by:
    Reducing travel costs
    Lowering logistic expenses

## Slide 39: Cluster Sampling
Application
Widely used in:
  Educational research
  Public health studies
Involves sampling entire groups such as:
  Classrooms
  Neighborhoods
Cost-effective
Time-saving
Especially beneficial for large populations by:
    Reducing travel costs
    Lowering logistic expenses

## Slide 40: Stratified Sampling
Enhances sampling precision for accurate results.

## Slide 41: Stratified Sampling
Enhances sampling precision for accurate results.
Applications
Used in social science
market research

## Slide 42: Sample Size Determination

## Slide 43
Exploratory Data Analysis (EDA)
in RStudio

## Slide 44
Descriptive Statistics
Date | Date of production (from 2025-04-01 onward)
Shift | Work shift during production (Morning or Evening)
Product | Beverage type: Aloe Juice, Energy Drink, or Protein Shake
Operator | The staff member responsible for operating the machine (e.g., Kevin, Mark)
Weight_g | Net weight of the filled bottle, measured in grams
Temperature_C | Temperature in degrees Celsius at the time of filling
Machine_ID | Machine used for filling the bottle (PX1, PX2, or PX3)
Defect | Whether the unit had a defect: 0 = No, 1 = Yes
Define Variables

## Slide 45
Qualitative Data Analysis : Shift, Product, Operator Factors, Machine

## Slide 46
Qualitative Data Analysis : Shift, Product, Operator Factors, Machine

## Slide 47
Qualitative Data Analysis : Shift, Product, Operator Factors, Machine

## Slide 48
Qualitative Data Analysis : Shift, Product, Operator Factors, Machine

## Slide 49
Qualitative Data Analysis : Weight
Statistic | Value
Mean | 499.7431 g
Median | 499.0250 g
Mode | 499.4500
Central Tendency

## Slide 50
Qualitative Data Analysis : Weight
Statistic | Value
Mean | 499.7431 g
Median | 499.0250 g
Mode | 499.4500
Statistic | Value
Minimum | 481.3700 g
Maximum | 529.2000 g
Range | 47.8300 g
Variance | 46.6801
Standard Deviation | 6.8323 g
1st Quartile (Q1) | 495.4775 g
3rd Quartile (Q3) | 502.4475 g
Interquartile Range (IQR) | 6.9700 g
Skewness | 0.81
Kurtosis | 1.31
Central Tendency
Spread of Data

## Slide 51
Qualitative Data Analysis : Weight
Statistic | Value
Mean | 499.7431 g
Median | 499.0250 g
Mode | 499.4500
Statistic | Value
Minimum | 481.3700 g
Maximum | 529.2000 g
Range | 47.8300 g
Variance | 46.6801
Standard Deviation | 6.8323 g
1st Quartile (Q1) | 495.4775 g
3rd Quartile (Q3) | 502.4475 g
Interquartile Range (IQR) | 6.9700 g
Skewness | 0.81
Kurtosis | 1.31
Central Tendency
Spread of Data

## Slide 52
Qualitative Data Analysis : Weight
Statistic | Value
Mean | 499.7431 g
Median | 499.0250 g
Mode | 499.4500
Statistic | Value
Minimum | 481.3700 g
Maximum | 529.2000 g
Range | 47.8300 g
Variance | 46.6801
Standard Deviation | 6.8323 g
1st Quartile (Q1) | 495.4775 g
3rd Quartile (Q3) | 502.4475 g
Interquartile Range (IQR) | 6.9700 g
Skewness | 0.81
Kurtosis | 1.31
Central Tendency
Spread of Data
Number of Outliers 44

## Slide 53
Qualitative Data Analysis : Temperature
Central Tendency
Statistic | Value
Mean | 23.51 °C
Median | 23.50 °C
Mode | 23.90 °C

## Slide 54
Qualitative Data Analysis : Temperature
Central Tendency
Statistic | Value
Mean | 23.51 °C
Median | 23.50 °C
Mode | 23.90 °C
Spread of Data
Statistic | Value
Minimum | 20.30 °C
Maximum | 26.30 °C
Range | 6.00 °C
Variance | 0.98
Standard Deviation | 0.99 °C
1st Quartile (Q1) | 22.88 °C
3rd Quartile (Q3) | 24.20 °C
Interquartile Range | 1.33 °C
Skewness | -0.08
Kurtosis | -0.11

## Slide 55
Qualitative Data Analysis : Temperature
Central Tendency
Statistic | Value
Mean | 23.51 °C
Median | 23.50 °C
Mode | 23.90 °C
Spread of Data
Statistic | Value
Minimum | 20.30 °C
Maximum | 26.30 °C
Range | 6.00 °C
Variance | 0.98
Standard Deviation | 0.99 °C
1st Quartile (Q1) | 22.88 °C
3rd Quartile (Q3) | 24.20 °C
Interquartile Range | 1.33 °C
Skewness | -0.08
Kurtosis | -0.11

## Slide 56
Qualitative Data Analysis : Temperature
Central Tendency
Statistic | Value
Mean | 23.51 °C
Median | 23.50 °C
Mode | 23.90 °C
Spread of Data
Statistic | Value
Minimum | 20.30 °C
Maximum | 26.30 °C
Range | 6.00 °C
Variance | 0.98
Standard Deviation | 0.99 °C
1st Quartile (Q1) | 22.88 °C
3rd Quartile (Q3) | 24.20 °C
Interquartile Range | 1.33 °C
Skewness | -0.08
Kurtosis | -0.11
Number of Outliers 5

## Slide 57
Qualitative Data Analysis : Temperature

## Slide 58
Weight Variation Across Operational Factors

## Slide 59
Weight Variation Across Operational Factors

## Slide 60
Weight Variation Across Operational Factors

## Slide 61
Weight Variation Across Operational Factors

## Slide 62
Factor-Wise Impact on Bottle Weight: ANOVA Analysis
Mean Weight Variation Across Product Types

## Slide 63
Factor-Wise Impact on Bottle Weight: ANOVA Analysis
Mean Weight Variation Across Product Types
Mean Weight Variation Across Product Types

## Slide 64
Factor-Wise Impact on Bottle Weight: ANOVA Analysis
Mean Weight Variation Across Product Types
Mean Weight Variation Across Product Types
Mean Weight Variation Across Product Types

## Slide 65
Factor-Wise Impact on Bottle Weight: ANOVA Analysis
Mean Weight Variation Across Product Types
Mean Weight Variation Across Product Types
Mean Weight Variation Across Product Types
Mean Weight Variation Across Product Types

## Slide 66
Factor-Wise Impact on Bottle Weight: Correlation and Regression Analysis

## Slide 67
Factor-Wise Impact on Bottle Weight: Correlation and Regression Analysis

## Slide 68
Factor-Wise Impact on Bottle Weight: Correlation and Regression Analysis

## Slide 70
Fishbone Diagram for Identifying
Causes of Underfilled Bottles

## Slide 71
Fishbone Diagram
Defects in underfilled bottles in production line
Material
Measurement
Machine
Method
Environment
Employee
Law quality Raw Ingredients
Packaging defects
Data collection errors
Control chart misinterpreted
Machine PX2 Inconsistency
Filling nozzle misalignment
Lack of standard operating procedure
Poor maintenance schedule
High ambient
temperature
Humidity
fluctuations
Lack of Training
Insufficient supervision
in evening shift
Low maintenance
Incorrect mixing ratios
Faulty weighing equipment

## Slide 72
Lean Six Sigma Application for
Process Optimization

## Slide 73
  Waste identification (7 Wastes)
  Our analysis revealed several types of waste impacting quality and efficiency.
  Defects

## Slide 74
  Waste identification (7 Wastes)
  Our analysis revealed several types of waste impacting quality and efficiency.
  Defects
  Waiting

## Slide 75
  Waste identification (7 Wastes)
  Our analysis revealed several types of waste impacting quality and efficiency.
  Defects
  Waiting
  Overproduction

## Slide 76
  Waste identification (7 Wastes)
  Our analysis revealed several types of waste impacting quality and efficiency.
  Defects
  Waiting
  Overproduction
  Over processing

## Slide 77
  Waste identification (7 Wastes)
  Our analysis revealed several types of waste impacting quality and efficiency.
  Defects
  Waiting
  Overproduction
  Over processing
  Motion

## Slide 78
  Waste identification (7 Wastes)
  Our analysis revealed several types of waste impacting quality and efficiency.
  Defects
  Waiting
  Overproduction
  Over processing
  Motion
  Inventory

## Slide 79
  Waste identification (7 Wastes)
  Our analysis revealed several types of waste impacting quality and efficiency.
  Defects
  Waiting
  Overproduction
  Over processing
  Motion
  Inventory
  Transportation

## Slide 80
Our process have these wastes
  Defects: 1.3% (29/2237), underfilled (<495g), sealing issues.

## Slide 81
Our process have these wastes
  Defects: 1.3% (29/2237), underfilled (<495g), sealing issues.
  Overproduction: Excess Energy Drink/Protein Shake output.

## Slide 82
Our process have these wastes
  Defects: 1.3% (29/2237), underfilled (<495g), sealing issues.
  Overproduction: Excess Energy Drink/Protein Shake output.
  Waiting: Delays from Machine PX2 inconsistency

## Slide 83
Process Bottlenecks Affecting Flow and Quality.
Filling
PX2 MACHINE
Sealing
Packaging
Frequent
sealing errors
Spike
Evening Shift
Delays
Operator
Higher defect rate
Process Bottlenecks

## Slide 84: Bottlenecks
Machine PX2: 37.9% defects (11/29)

## Slide 85: Bottlenecks
Machine PX2: 37.9% defects (11/29)
Evening Shifts: 62.1% defects (18/29)

## Slide 86: Bottlenecks
Machine PX2: 37.9% defects (11/29)
Evening Shifts: 62.1% defects (18/29)
Underfilling: EnergyDrink (55.2%)

## Slide 87: Findings & Root Causes
Findings:
  Defect Rate: 1.3% (DPMO ≈ 13,000)
  PX2: 37.9% defects, SD 4.5g (Energy Drink)
  Evening Shifts: 62.1% defects
Machine
PX2 Variability
Root Causes of Defects

## Slide 88: Findings & Root Causes
Findings:
  Defect Rate: 1.3% (DPMO ≈ 13,000)
  PX2: 37.9% defects, SD 4.5g (Energy Drink)
  Evening Shifts: 62.1% defects
Machine
PX2 Variability
Method
Evining Process
Root Causes of Defects

## Slide 89: Findings & Root Causes
Findings:
  Defect Rate: 1.3% (DPMO ≈ 13,000)
  PX2: 37.9% defects, SD 4.5g (Energy Drink)
  Evening Shifts: 62.1% defects
Machine
PX2 Variability
Method
Evining Process
Method
Operator Training
Root Causes of Defects

## Slide 90: Findings & Root Causes
Findings:
  Defect Rate: 1.3% (DPMO ≈ 13,000)
  PX2: 37.9% defects, SD 4.5g (Energy Drink)
  Evening Shifts: 62.1% defects
Machine
PX2 Variability
Method
Evining Process
Method
Operator Training
Method
Bottle fill issue
Root Causes of Defects

## Slide 91
How we reduced variation and improved process

## Slide 92
Used the DMAIC Method
PX2 inconsistency Hourly checks +maintenance

## Slide 93
Used the DMAIC Method
PX2 inconsistency Hourly checks +maintenance
Sealing issues (Evening) SOP for cleaning & pressure

## Slide 94
Used the DMAIC Method
PX2 inconsistency Hourly checks +maintenance
Sealing issues (Evening) SOP for cleaning & pressure
Operator variation Retrain with visual guides

## Slide 95
Used the DMAIC Method
PX2 inconsistency Hourly checks +maintenance
Sealing issues (Evening) SOP for cleaning & pressure
Operator variation Retrain with visual guides
Manual weight checks Sensor based feedback loop